Model Question Paper-2006

NATIONAL CERTIFICATION EXAMINATION

FOR

ENERGY MANAGERS & ENERGY AUDITORS

PAPER – 1: General Aspects of Energy Management & Energy Audit Duration: 3 HRS Max. Marks: 150

# Section – I:	 OBJECTIVE TYPE 				Marks: 50 x 1 = 50

(i)	Answer all 50 questions

(ii)	Each question carries one mark

(iii)	Put a (() tick mark in the appropriate box in the answer book

| 1. | The fuel type, which is fastest growing among world energy consumption a) Coal b) Oil c) Natural Gas d) Nuclear Energy |
| --- | --- |
| 2. | The percentage of primary energy consumption of India in the total world energy consumption is a) 3.5 % b) 7 % c) 10.5 % d) 1 % |
| 3. | What is the current Reserves/Production ratio of coal in India a) 180 b)200 c) 230 d) 290 |
| 4. | The % of crude oil import bill of India in the year 2020 will be . 72. b) 77 c) 82 d) 92. |
| 5. | Which one of the following is not considered as a pollutant a) CO2 b) SO2 c) CO dVOCs |
| 6. | The major contribution of CO pollutant In the urban area is due to a) 90 % of industrial pollution b) 90 % of road transport c) 90 % residential and commercial d) all of the above |
| 7. | CAGR means a) Compound annual growth rate b) Compound average growth rate c) Compound annual growth ratio d) Compound average growth ratio |
| 8. | What is the heat content of the 200 liters of water at 50oC in terms of the basic unit of energy in K.Joules a) 3000 b) 2388 c) 1000 d) 4187 |
| 9. | What is the heat required to melt 2 kg of ice from Zero degree to liquid water at zero degree in KJ ? a)672 b) 6000 c) 6048 d) 8374 |
| 10. | The rate of energy transfer is measured in a) Jules/Second b) K.Cal/hr c) BTU/hr d)all of the above |
| 11. | Which of the following is most accurate instrument for surface temperature measurement of the hot pipe line Thermocouples c) Infrared Thermometer Leaf type contact thermometer d) All of the above |
| 12. | Which one of the following is not considered for external benchmarking : a) Scale of Operation b) Vintage of Technology c) Energy Price d) Quality of Raw Material and Products |
| 13 | In inductive and resistive circuit, the effective power factor will be a) less than 1 b) more than 1 c) zero d) one |
| 14. | Which of the following factor to be taken into account while procurement of fuel ? a) Gross Calorific Value b) Moisture content c)Cost at Site d) All of the above |
| 15. | A single phase 2.5 hp AC motor has the name plate details as 230v,10 amps and PF 0.8. the operating details are 220Volt, 8 amps and 0.7 PF what is the % loading of motor a) 67% b) 77 c) 80 d) 60 |
| 16. | Which are the following is not correct as per Law of Conservation of Mass ? a) Mass in = Mass out + Mass Stored b) Raw material in = Product + Waste + Stored Material c)Raw material in = Product + Waste + Stored material + Internal Recycling d) All are the above |
| 17 | Which of the following formula is useful to determine the heat duty in conducting heat balance? a) Q = M.Cp.Δ T b) Q = AV c) PV = n RT d) None of the above |
| 18 | Utilization of Solar drying instead of washing machine for clothe drying purpose is called a) Energy substitutions b)Energy efficiency measure c) Fuel substitution d) None of the above |
| 19 | The velocity of cold air in the air-conditioning duct can be measured by a) pitot tube b) anemometer c) both a & b d) none of the above |
| 20 | Which one of the following is not important to the successful energy management in all organizations? a) Top management support b) Good Monitoring system c) Strategic Planning d) Procuring low cost energy |
| 21. | Which one of the following is not an important duty of a certified energy manager ? a) Report to BEE and State level designated agencies b) Prepare a scheme for efficient use of energy c) Establish an improved data recording and analysis d) Create knowledge bank on sectoral and national development on energy efficiency technology and information |
| 22 | Which of the following is not common normalizing factor in industrial facilities? a) Input b) Output c) Product type d) Operating hours |
| 23 | Which of the following is a negative force in force field analysis? a) High price of energy b) High energy share of component of production cost c) Availability of energy efficient technology d) Competing corporate priorities |
| 24 | Which of the following equation can be used to calculate the future value from the present value of cash.? a) NPV = FV x (1 + i)n b) FV= NPV x (1 - i)n c) NPV =FV/ (1 + i)n d)NON OF THE ABOVE. |
| 25 | What is the expected ROI from the project with Rs.5 lakhs investment and annual saving of Rs.1.75 lakhs and annual operating cost of Rs.0.25 lakhs a) 25 b) 30 c) 35 d) 40 |
| 26 | ESCO means a) Energy saving companies b) Energy service companies c) Energy supply companies d) Energy saving corporation |
| 27 | A 500 kg of wet cloth with 50% moisture at 25o is dried to 5% moisture in stenter steam drying machine. What is the moisture content removed from the cloth ? a) 237 b) 263 c) 275 d) 225 |
| 28 | Which of the following is not considered in CPM method Network Diagram? a) Duration of each activities b) Dependency of activities c) Time variation d) None of the above |
| 29 | Which of the following condition is useful to determine the critical path in the PERT Network ? a) ES = LS and EF = LF b) ES = LF and EF = LS c) ES= EF and LS = LF d) None of the above |
| 30 | Which is not a fast track CDM Projects among the following ? a) Biomass Power Plant up to 15 MW b) Photovoltaic Power Plant up to 15 MW c) Plantation Project upto 15 kiloTon of CO2 equivalent reduction annually d) Energy efficiency improvement projects up to 15 MW Power Reduction annually |
| 31 | Ozone layer is found in the stratosphere between a) 5 to 50 km above the ground b) 10 to 50 km above the ground c) 50 to 100 km above the ground d) 10 to 100 km above the ground |
| 32 | In a heat treatment furnace 500 kg/hr. iron material is heated from 27.5oC to 850oC. Specific heat of the material is 1.8 K.cal/ kg. oC What is the heat duty in KW? a) 500 b) 900 c) 860 d) None of the above |
| 33 | In a chemical process reactant A and B are mixed in the ratio of 100 kg:200 kg. The yield will be resulted in the ratio of 50 : 50 . What is the amount of yield in kg? a) 100 b)150 c) 200 d) 300 |
| 34 | Which of the following is a macro factor for sensitivity analysis? a) change in capital structure b) change in project duration c) changes of the firms of finance d) change in tax rates |
| 35 | Sensitivity analysis is carried out for which purpose of the following assessment? a) Profit b) Losses c) risk d) all of the above |
| 36 | A factor that reflects the risk of the project while evaluating the net present value for the expected future cash flow is: a) Discount rate b) Internal rate of return c) Capital Cost d) All of the above |
| 37 | The annual electricity bill for a plant is Rs. 40 lakhs and accounts for 25% of the total energy bill. The annual energy bill for the company a) ) Rs. 40 lakhs b) Rs. 80 lakhs c) Rs. 160 lakhs d) none of the above |
| 38 | Critical path in a PERT network diagram a) is the shortest path in a network b) where all activities of long duration fall c) path that has no slack for all activity in that path d) none of the above. |
| 39 | Matching energy use to requirement means providing a) just providing theoretical energy needed b) just the designers’ needs c) energy with minimum losses d) all of the above |
| 40 | The internal rate of return is the discount rate for which the NPV is a) Zero b) positive c) Negative d) None of the above |
| 41 | The fixed energy consumption plant is 5000 Kwh. The specific energy consumption of the product is 1200 Kwh/Ton . What is the total energy consumption for the production of 100 Tons / day? a) 120,000 b) 125,000 c) 6,200 d) 50,000 |
| 42 | The last step in a project development cycle is a) Identify components of the project b) Implement the project c) arrange finance d) Close out the project |
| 43 | For an investment which has a fluctuating savings over its project life which of these analysis would be the best option a) SPP b) ROI c) NPV d) none of the above |
| 44 | Data required to plot a moving annual total chart a) Month wise production b) Month wise energy consumption c) Both a & b d) Annual production & annual energy consumption |
| 45 | What is the “toe” of 125 Ton of coal which has GCV of 4000 K.cal / kg a) 40 b) 50 c) 400 d) 500 |
| 46 | How many molecules are destroyed by a single CFC molecules before it depletes. a) 101 b) 103 c) 105 d) 107 |
| 47 | ODS means a) Ozone depleting substances b) Ozone diluting substances c) Ozone disturbed space d) None of the above |
| 48 | GWP of Nitrous Oxide component CO2 a) 21 b) 210 c) 27 d) 270 |
| 49 | India comes under which of the following category as per Kyoto protocol a) Annex I Parties b) Annex 2 Parties c) Annex 1 & 2 Parties d) Non Annex Parties |
| 50 | What is the size of the market for emission reduction in the world is a) one million ton of carbon reduction by during the commitment period 2008-2012 b) one billion ton of carbon reduction by during the commitment period 2008-2012 c) one billion ton of carbon reduction by during the commitment period 2005-2010 d) one trillion ton of carbon reduction by during the commitment period 2005-2010 |

# Section - II: 	  SHORT DESCRIPTIVE QUESTIONS		Marks: 10 x 5 = 50

(i)	Answer all Ten questions

(ii)	Each question carries Five marks

S-1	(i) List down the role of state and central govt in implementation of Energy conservation act 2001?

(ii) What is energy conservation building s code?

S-2	What are the different phases of detailed energy audit and list down the aims of the preliminary site visit?

S-3	An insulated Electric heater of 6 KW was replaced with low pressure steam heater for furnace oil heating in Thermic fluid heating system .The avg electricity consumption per day is 120 kwh.  Find out the quantity of steam consumption if steam at temperature 121oc with enthalpy of 642 kcal/kg and per day. Electricity cost is 4Rs/unitPlant steam cost is Rs 0.50/kg. What is cost reduction per day?

S-4	 What is an objective of the energy policy in an organization? List down the typical format of energy policy

S-5	Explain Quantitative Reviews  and Qualitative Reviews while analyzing after conducting energy audit?

S-6	Define the IRR of a project and indicate its limitation and advantages.

S-7	Cold Air at 25oC is supplied through  a square duct to a air-conditioning building .  The velocity and quantity of cold air flow are 2 m/s  and 250 m3/ hr.  respectively.  Find out the size of the square duct in mm.

S-8	 What are the 3 time estimate used for constructing PERT Network? One of the activity has  3 time estimate of 4 weeks, 5 weeks and 6 weeks  in a PERT Network diagram.  Find out the expected time to complete the activity  and it’s variance of the activity

S-9	What are the Global warming implications and how India could affect by this climatic change?

S-10	(i) What is the sensitivity analysis?  List down 4 micro factors that are considered in the above analysis.

-------- End of Section  - II ---------

Section - III: 	  LONG DESCRIPTIVE QUESTIONS                Marks: 5 x 10 = 50

(i)	Answer all Five questions 	(ii)	Each question carries Ten marks

L-1	Find out the mass fraction and mole fraction of Carbon dioxide in the Carbonated soft drink preparation.  If 2 volume of CO2 is mixed with 1 volume of water at 0o and atmospheric pressure gas content  = 0.08206.

L-2	What are the elements of monitoring and targeting system ?  Explain how to draw moving annual total method.  What is the inference of this method?

L-3	A company has  invested Rs.20 lakhs for installing WHR Boiler to recover waste heat from the flue gas in DG  Set.  Find out the IRR  if the annual net savings cash flow accrued for  6 years as given below: The company got a bank loan  for the investment  at 8% interest rate.  Whether the company can recover the investment and repay the bank loan.

| Year | Annual Net Saving, Rs. lakhs |
| --- | --- |
| 1 | 6 |
| 2 | 6 |
| 3 | 7 |
| 4 | 7 |
| 5 | 8 |
| 6 | 8 |

L-4	Construct a PERT Diagram for the following projects and find out the critical path.  If an activity duration of G is reduced by 2 days, what is the new critical path and completion of time.?

| Activity | Duration in Days | Precedent |
| --- | --- | --- |
| A | 2 | Start |
| B | 3 | A |
| C | 5 | A |
| D | 4 | B |
| E | 6 | B |
| F | 5 | C |
| G | 7 | D |
| H | 3 | E |
| I | 1 | F, G, H |

- What is the critical path?

- What is the total duration required to complete the project?

- What is the available slack period in days for activity C & E?

- If duration of activity G is reduced by 2 days by crashing, what is the new critical path and it’s duration of the project completion?

L-5	How CDM works and what are the CDM initiatives   in India

-------- End of Section  - III ---------